## Slide 1: SystemVerilog HDL Workshop #1
044252 - Digital Systems and Computer Structure

## Slide 2
Industry positions
RTL/Logic Design/Front end Engineer
Chip design verification
Clock Engineer
Integration Engineer
SDC timing Engineer (Backend)

## Slide 3: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 4: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 5
Logic Gates – A Reminder

## Slide 6: Ways to Represent Hardware:
Hardware Description Language
Netlist
Schematic drawing
Truth table
nand(Z, X, Y);
logic Z;
assign Z = X ~& Y;
logic Z;
always_comb
if (X) Z = ~Y;
else Z = 1;
X | Y | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 7: Hardware Description Languages (HDLs)
Textual representation of digital circuits
HDLs are not “programming languages”
  No, really. Even if they look like it, they are not.
Similar development chain to software
  Software: Compiler
    Source code  Assembly code  Machine code
  Hardware: Synthesizer
    HDL Source  Netlist  Hardware

## Slide 8: Why Use an HDL?
Easy to write and edit
Compact
Don’t have to follow a maze of lines
Easy to analyze with various tools

## Slide 9: SystemVerilog
Superset of Verilog
One of the two leading HDLs - VHDL is the other.
Most digital chips are designed in part using one of these two languages

## Slide 10: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 11: Modules
module: fundamental building block
  Describes a digital circuit
  Hierarchical modules contain (instantiate) other modules
f
in1
in2
inN
out1
out2
outM
my_module
Everything you write in SystemVerilog must be inside a module!

## Slide 12: Modules
module my_module(
output logic out1,
output logic out2,
...,
input logic inN
);
... // declarations
... // description of f
endmodule
Module Name
Input and Output Declaration
f
in1
in2
inN
out1
out2
outM
my_module
No ; !
Module Start & End
Notes: לדבר על interface

## Slide 13: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 14: The Logic Data Type
The logic data type represents a wire (1 bit)
Declaring a logic variable:
a
b
c
d
e
logic a, b, c, d; logic e;

## Slide 15: The Logic Data Type
In this course, we will use the logic data type
More data types in SystemVerilog (not recommended!)
  wire
  reg
  integer
  time
  More…
logic type replaces both wire and reg

## Slide 16: SystemVerilog Logic Values
0: zero / logic low / false / ground
1: one / logic high / true / power
x: not initialized or collision
z: unconnected

## Slide 17: Reminder: 41 Selector /Multiplexer / Mux
Input: | 2 Control inputs
 | 22 Data inputs
 | Enable input
Output: | if E=0 then ‘0’
 | else DS
E
How to represent several bits?
O
Notes: מה זה mux?

## Slide 18: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 19: Vectors
Declaration of an 8-bit logic vector:
Exercise: write a mux module declaration
logic [7:0] w1; // w1[7] is the MSB
O

## Slide 20: Mux Module Declaration - Solution
module mux4to1(
output logic O,
input logic D0,
input logic D1,
input logic D2,
input logic D3,
input logic E,
input logic [1:0] S
);
... // declarations
... // description of a mux
endmodule
O

## Slide 21: Vector Operations
  Bit select:
  Range select:
  Pack:
  Unpack:
vec = {x, y, z};
{carry, sum} = vec[1:0];
w1[3]
w1[3:2]

## Slide 22: Vectors - Exercise
Swap high and low nibbles of w1 into w2
Solution:
logic [7:0] w1; logic [7:0] w2;
w2 = {w1[3:0], w1[7:4]};

## Slide 23: Intro – 2’s complement
N-bit Unsigned binary:
N-bit Signed binary:
The only difference is the MSB changes to a negative value!
Example: 1010 Example: 11010
Unsigned: 8+2 = 10 Unsigned: 16+8+2 = 26
Signed: -8+2 = -6 Signed: -16+8+1 = -6

## Slide 24: Repeated Signals
Previously we discussed vector concatenation:
We can also repeat a signal n times:
vec = {x, y, z};
vec = {16{x}}; // 16 copies of x

## Slide 25: Repeated Signals - Example
Question: What does this do?
Answer: Unsigned extension
Question: What about this?
Answer: Signed extension
logic [7:0] out; logic [3:0] A; out = {{4{1’b0}}, A[3:0]};
out = {{4{A[3]}}, A[3:0]};

## Slide 26: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 27: Module Implementation
There are 3 ways to implement hardware inside a module:
  Module instantiation
  Concurrent assignments
  Procedural blocks

## Slide 28: Module Instantiation
Implementing a module using other modules as building blocks
My Module
Module
Building Block #1
Module
Building Block #2
input1
output1

## Slide 29: Module Instantiation
Implementing a module using other modules as building blocks

## Slide 30: Module Instantiation – Interview question
Given Module MAX(A,B):
implement a device which finds the value order of 4 numbers A,B,C,D using minimal number of Modules.
The maximum will be located on the lowest wire
A
B

## Slide 31: Module Instantiation – Interview question
A
B
C
D

## Slide 32: Module Instantiation Syntax
module_name instance_name1 (
my_out1,
my_out2,
...,
my_inN
);
Positional association:
Named association:
module_name instance_name2 (
.out1(my_out1),
.out2(my_out2),
...,
.inN(my_in1)
);
044252 - Digital Systems and Computer Structure - SystemVerilog HDL Workshop
32
Instance name
Input and Output port assignments
Module name
Module port name
Wire name
Module name
Instance name

## Slide 33: Module Instantiation Example
top
mymodule
A
B
C
mymodule
A
B
C
inst1
inst2
net1
net2
net3
net4
net5
module mymodule (
output logic C,
input logic A,
input logic B
);
…
…
endmodule
module top;
logic net1, net2, net3, net4, net5;
…
mymodule inst1 (net4, net1, net2);
mymodule inst2 (.C(net5), .A(net2), .B(net3));
…
endmodule
Connect by name
Use this only!
Connect by position

## Slide 34: Built-in SystemVerilog Modules
Basic logic gates available for direct instantiation
  and
  or
  not
  xor
  nand
  nor
  xnor
Syntax: gateName(output, input1, <input2>)
not(O1, A);
nor(O2, A, B);

## Slide 35: Example – Half Adder Implementation

## Slide 36
module HA (
output logic S,
output logic C,
input logic A,
input logic B
);
xor(S, A, B);
and(C, A, B);
endmodule
Example – Half Adder Implementation

## Slide 37: Module Instantiation Example
What we have:
Build complex modules using simpler modules
S
O

## Slide 38: Module Instantiation Example
What we need:
A0
Implement 4->1 Mux using minimal number of 2->1 mux.
S0
O
A1
A2
A3
S1

## Slide 39: Module Instantiation Example
Implement 4->1 Mux using minimal number of 2->1 mux.
A0
S0
A1
A2
S0
A3
S1

## Slide 40: Module Instantiation Example
2-bit wide mux from two 1-bit muxes
  Just “drawing” boxes and wires
  module mux2to1_2 (
  output logic [1:0] O,
  input logic [1:0] A,
  input logic [1:0] B,
  input logic S
  );
  mux2to1 mux0 (.O(O[0]), .S(S), .A(A[0]), .B(B[0]));
  mux2to1 mux1 (.O(O[1]), .S(S), .A(A[1]), .B(B[1]));
  endmodule
Module Name
Instance Name
Input Port Name
Input Port Assignment
B[1:0]
S
O[1:0]
A[1:0]
A]0[
B]0[
A]1[
B]1[
O]0[
O]1[
O
O
S
S

## Slide 41: The generate Command
Implementation of a 32-bit wide mux from 32 1-bit muxes using regular instantiation is long and exhausting…
  Use generate
module mux2to1_32 (
output logic [31:0] O, // Output bits O
input logic [31:0] A, // Input bits A
input logic [31:0] B, // Input bits B
input logic S // Select
);
genvar i;
generate
for (i = 0; i < 32; i++)
begin
mux2to1 mux_inst(.O(O[i]), .S(S),
.A(A[i]), .B(B[i]));
end
endgenerate
endmodule

## Slide 42: Agenda
Hardware Description Languages
SystemVerilog Building Blocks:
  Modules
  The logic data type
  Vectors
  Module implementation
    Module instantiation
Test benches and simulation

## Slide 43: SystemVerilog: design vs. simulation
Simulation = a way to test the design
Initial begin
#1 a = 1;
#3 b = 1;
#5 a = 0;
…
end

## Slide 44: How Are Simulators Used?
Testbench generates stimuli and checks response
Testbench
Response
Module Instance
(UUT)
.
.
.
InputN
Input1
.
.
.
OutputM
Output1
Stimuli

## Slide 45: Test Bench - Generating Stimuli
Data: A sequence of values
initial begin
data = 0;
#50
data = 1;
#30
data = 0;
#20
data = 1;
end

## Slide 46: Test Bench
module HA_tb;
logic ha_a;
logic ha_b;
logic ha_sum;
logic ha_carry;
HA uut (
.a(ha_a),
.b(ha_b),
.sum(ha_sum),
.carry(ha_carry)
);
initial begin
ha_a = 0;
ha_b = 0;
20#
ha_a = 1;
ha_b = 0;
20#
ha_a = 0;
ha_b = 1;
20#
ha_a = 1;
ha_b = 1;
end
endmodule
Stimuli Signals Creation
Tested Module Instantiation
Stimuli Generation
Testbench
Module Instance
(UUT)
.
.
.
InputN
Input1
.
.
.
OutputM
Output1
Stimuli

## Slide 47: Wet Exercise 0
You will be required to:
  Get to know ModelSim
  Fix bugs in a HA implementation
  Test it using a simulation
The videos are recommended
The workshops cover all the syntax needed to solve the wet exercise

## Slide 48: Summary

## Slide 49: Questions?

## Slide 50: Workshop #1 Cheat Sheet
Module:
Logic:
Logic values: 0, 1, x, z
Vector:
module my_module(
output logic ...,
input logic ...
);
... // declarations
... // description of a mux
endmodule
logic a, b, c, d;
logic [7:0] w1; // w1[7] is the MSB

## Slide 51: Workshop #1 Cheat Sheet
Vector operations:
  Bit select
  Range select
  Pack
  Unpack
  Repeated signals
vec = {x, y, z};
{carry, sum} = vec[1:0];
w1[3]
w1[3:2]
vec = {16{x}}; // 16 copies of x

## Slide 52: Workshop #1 Cheat Sheet
Module instantiation:
Built-in logic gates:
module_name instance_name1 (
.out1(my_out1),
.out2(my_out2),
...,
.inN(my_in1)
);
not(O1, A);
nor(O2, A, B);

## Slide 53: Workshop #1 Cheat Sheet
Generate:
genvar i;
generate
for (i = 0; i < 32; i++)
begin
mux2to1 mux_inst(.out(O[i]), .sel(sel),
.A(A[i]), .B(B[i]));
end
endgenerate