## Slide 1: SystemVerilog HDL Workshop #2
044252 - Digital Systems and Computer Structure

## Slide 2: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 3: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 4: Integer Literals in SystemVerilog
<width'><signed><radix> value (”<>” indicates optional part)
  Defaults
    Width = 32
    Unsigned
    Radix = Decimal
Number of
bits
Binary  b or B
Octal  o or O
Decimal  d or D
Hexadecimal  h or H
Consecutive chars
0-f, x, z
s,S – Signed
(Two’s
complement)

## Slide 5: Integer Literals in SystemVerilog
<width'><signed><radix> value
1'b0
  one bit with an unsigned value of zero
8'hFF
  8 bits with an unsigned value of 0xFF (or 255 in decimal)
14
  32 bits with an unsigned value of 14 in decimal
-14
  32 bits with a signed value of -14

## Slide 6: Integer Literals in SystemVerilog
<width'><signed><radix> value
4'sb1011
  4 bits with a signed value of -5
12'b1010_1101_0001 = 12'hAD1
  12 bits with an unsigned value of 2769 (underscores are ignored)

## Slide 7: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 8: Bitwise Operators (i)
&  bitwise AND
|  bitwise OR
~  bitwise NOT
^  bitwise XOR
~^ or ^~  bitwise XNOR
Operation on bit by bit basis

## Slide 9: Bitwise Operators (ii)
c = ~a;
c = a & b;
a = 4'b1010;
b = 4'b1100;
a = 4'b1010;
b = 2'b11;
c = a ^ b;

## Slide 10: Shift
>>  shift right
<<  shift left
a = 4'b1010;
  b = a << 2; // b = 4'b1000
  c = a >> 1; // c = 4'b0101

## Slide 11: SystemVerilog Operator Precedence

## Slide 12: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 13: Module Implementation
There are 3 ways to implement hardware inside a module:
  Module instantiation
  Concurrent assignments
  Procedural blocks – “Processes”

## Slide 14: 2. Concurrent Assignments
Connect a wire to a combinational logic or another wire
When the right-hand-side of an assignment changes, it immediately flows through to the left-hand-side wire
Syntax:
logic signal;
assign signal = 1'b0;
logic signal1;
logic signal2;
assign signal2 = signal1;

## Slide 15: Concurrent Assignment Example #1
module buffer_module (
output logic Z,
input logic A
);
assign Z = A;
endmodule

## Slide 16: Concurrent Assignment Example #2
module and_module (
output logic Z,
input logic A,
input logic B
);
assign Z = A & B;
endmodule

## Slide 17: Concurrent Assignment Example #3
module logic_module (
output logic Z,
input logic A,
input logic B,
input logic C
);
assign Z = (A & B) | C;
endmodule

## Slide 18: Interview question
module mymodule (
output logic [31:0] data_out,
input logic [31:0] data_in1,
input logic [31:0] data_in2,
input logic request1,
input logic request2
);
//complete your code here
endmodule
This module receives 2 request inputs and 2 data input. Output should be the input data of the correspond request. Complete module implementation without using
If/else statements.

## Slide 19: Interview question
module mymodule (
output logic [31:0] data_out,
input logic [31:0] data_in1,
input logic [31:0] data_in2,
input logic request1,
input logic request2
);
assign data_out = (data_in1 & {32{request1}}) + (data_in2 & {32{request2}});
endmodule
This module receives 2 request inputs and 2 data input. Output data should be the input data of the correspond request. Complete module implementation without using
If/else statements.

## Slide 20: Module Implementation
There are 3 ways to implement hardware inside a module:
  Module instantiation
  Concurrent assignments
  Procedural blocks – “Processes”

## Slide 21: 3. Procedural Blocks
Sequential: all statements inside the block are executed sequentially
  One line after the other
Two procedural constructs:
  initial
  always_comb

## Slide 22: Procedural Blocks – Initial Statement
initial statement is executed only once. We will use it only in simulations.
Syntax:
initial begin
<statement1>;
# time_to_wait
<statement2>;
# time_to_wait
...
end

## Slide 23: Procedural Blocks – Initial Statement Example
module mymodule_tb;
logic a;
logic out;
mymodule uut (
.a(a),
.out(out)
);
initial begin
a = 1'b0;
5#
a = 1'b1;
5#
a = 1'b0;
end
endmodule

## Slide 24: Procedural Blocks – always_comb Statement
always_comb statement: Executed sequentially. Used for combinational logic implementation. It guarantees that the logic will be treated as purely combinational and ensures no unintended latches are inferred .
Syntax:
always_comb begin
<statement1>;
<statement2>;
...
end

## Slide 25: Procedural Blocks – always_comb Statement Example
module and_module (
output logic Z,
input logic A,
input logic B
);
always_comb begin
Z = A & B;
end
endmodule
Note: no assign!

## Slide 26: Another Example - Shift
module shift_module (
output logic [3:0] out,
input logic [3:0] a
);
always_comb begin
out = a << 2;
end
endmodule

## Slide 27: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 28: Parameters
Allow per-instantiation module parameters
  Use “parameter” statement
Syntax:
module_name #(
.param1(value1),
.param2(value2),
.param3(value3)
) instname (
.in1(in1),
...
.out1(out1)
;(
Module Declaration:
Module Instantiation:
module module_name (
output logic out1,
...,
input logic in1
);
parameter param1 = 1;
parameter param2 = 2;
parameter param3 = 3;
...
endmodule
Note: instantiation of params

## Slide 29: Parameters: Example
module shift_N (
output logic [3:0] out,
input logic [3:0] a
);
parameter N = 1;
always_comb begin
out = a << N;
end
endmodule
module shifts (
output logic [3:0] b,
output logic [3:0] c,
input logic [3:0] a
);
  shift_N #(
  .N(2)
  ) shift_inst1 (
  .a(a),
  .out(b)
  ;(
  shift_N #(
  .N(3)
  ) shift_inst2 (
  .a(a),
  .out(c)
  ;(
endmodule

## Slide 30: Example for using Parameters in the Wet Exercise
module my_module (...);
...
AND2 #(
.Tpdhl(2), .Tpdlh(3)
) and_ist (
.Z(and_out),
.A(a),
.B(b)
);
endmodule
module AND2 (
output logic Z,
input logic A,
input logic B
);
parameter Tpdhl = 1;
parameter Tpdlh = 1;
...
endmodule
Using a logic gate with a propagation delay:
Unless stated otherwise, the hardware is ideal (Tpd = 0)!

## Slide 31: Local Parameters
Contain constant values
Cannot be assigned during instantiation - not to be confused with parameters
Syntax:
Example:
module my_module (...);
localparam N = 2'b11;
localparam NUM_OF_CYCLES = 10;
...
endmodule
localparam <param_name> = <param_value>;

## Slide 32: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 33: Parallelism in HDL
Hardware Description Language describes hardware
Each of the 3 ways to implement a module describes a hardware part of the module
All hardware parts “live” concurrently!
Statements in a module (outside of procedural blocks) simply define existence and not executed sequentially
The order of appearance is not important

## Slide 34: Examples of Parallelism in HDL
module my_module (
output logic a,
output logic b
);
assign a = 1'b0;
assign b = 1'b0;
assign a = 1'b1;
endmodule
Compilation Error

## Slide 35: Examples of Parallelism in HDL
module my_module (
output logic c
);
logic a;
logic b;
assign c = a | b;
assign a = 1'b0;
assign b = 1'b1;
endmodule
c = 1'b1

## Slide 36: Combinational Example: Mux Implementation
in
2
In[0]
In[1]
outn

## Slide 37: Combinational Example : Mux Implementation
module mux (
output logic out,
output logic outn,
input logic [1:0] in,
input logic sel
);
logic out1, out2, selb;
and a1 (out1, in[0], sel);
not i1 (selb, sel);
and a2 (out2, in[1] , selb);
always_comb begin
out = out1 | out2;
end
assign outn = ~out;
endmodule
in
2
In[0]
In[1]
outn

## Slide 38: System Tasks
$display: prints arguments in the console window
$time: gives the simulation time
$stop: stops the simulation

## Slide 39: System Tasks - Example
module and_module_tb;
logic a;
logic b;
logic c;
and_module and_module_inst(.a(a), .b(b), .c(c));
initial begin
a = 1'b0;
b = 1'b1;
$display("%t: a = %d, b = %d, c = %d", $time, a, b, c);
$stop;
end
endmodule
module and_module (
output logic c,
input logic a,
input logic b
);
assign c = a & b;
endmodule

## Slide 40: Agenda
SystemVerilog building blocks:
  Values / number representation
  Operators
  Module implementation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Common mistakes

## Slide 41: Common Mistake #1 – Thinking a Module is a Function Call
module my_module(...);
...
logic w;
mux2to1 mux0 (.sel(sel), .A(a1), .B(b1), .out(w));
endmodule
w
a1
b1
This is instantiation, not a function call!
Notes: בפונקציה ניתן להזין 2 שורות באותם פרטמטרים, בסיסטם ורילוג זה ייצר לנו חוטים ויצור שגיאה
בפונקציה אפשר לעשות קריאה פעמיים ולדרוס ערכים קיימים, כאן זה יגרום להתנגשות חוטים

## Slide 42: Common Mistake #2 – Connecting Wires
The same wire cannot be connected to two different module outputs!
module my_module(...);
...
logic w;
mux2to1 mux0 (.sel(sel), .A(a1), .B(b1), .out(w));
mux2to1 mux1 (.sel(sel), .A(a2), .B(b2), .out(w));
endmodule
w
a1
b1
a2
b2
w
w

## Slide 43: Common Mistake #2 – Connecting Wires
The same wire cannot be connected to two different gate outputs!
module my_module(...);
...
logic w;
logic a;
logic b;
assign w = a & b;
assign w = a | b;
endmodule
w
a
b
a
b

## Slide 44: Common Mistake #2 – Connecting Wires
The same wire cannot be connected to two different gate outputs!
module my_module(...);
...
logic w;
logic a;
logic b;
always_comb begin
w = a & b;
end
always_comb begin
w = a | b;
end
endmodule
w
a
b
a
b

## Slide 45
Common Mistake #2 – Connecting Wires
Collision may cause ‘x’ values in simulation
Notes: איקסים באמצע סימולציה מצביע על שגיאה! איקסים בהתחלה – לגיטימי בגלל זמני זיהום והשהיה

## Slide 46: Common Mistake #3 – Wrong Debugging
When there are bugs, check internal modules first!
module my_module(...);
...
logic w1;
logic w2;
mux2to1 mux0 (.sel(sel), .A(a1), .B(b1), .out(w1));
mux2to1 mux1 (.sel(sel), .A(a2), .B(b2), .out(w2));
endmodule
w1
a1
b1
a2
b2
w2
my_module
Notes: בסיסטם ורילוג אין לנו אותה "זמינות" לטסטים כמו שיש לנו בשפת סי או פייטון
לכן, מה שנעשה זה לבדוק את האינסטנסים הפנימיים.
תכתבו טסט למוקס 2 לפני שאתם ממשים את מוקס 4.

## Slide 47: Common Mistake #4 – Not Being a ModelSim Superuser
Use the command line
Notes: השתמשו בשורת הפקודה
כאשר משתמשים בשורת פקודה ניתן לעזור לכם

## Slide 48: More Common Mistakes
Can be found in the FAQ file in the Moodle course website

## Slide 49: Writing Code in SystemVerilog
Use your favorite text editor to implement your design
  Notepad++ is recommended
Every module is in a separate file that has the name of the module
  e.g., my_module.sv implements my_module
module my_module (...);
// Implementation
endmodule
my_module.sv

## Slide 50: How to Debug Your Code?
Add all the relevant signals to the waveform
Check all the relevant inputs/special cases
  If you can’t check all – check special cases
Look for suspicious behavior
  Signals with ‘x’ value: did you forget to initialize them? Is it a collision? Or does it make sense? (Tpd, …)
  Signals with ‘z’ value: probably forgot to connect a wire

## Slide 51: How to Add Internal Signals to the Waveform?
1. Navigate to the module instance in the “sim – Default” window and mark it
2. In the “Objects” window, Right click on the relevant signal and choose “Add Wave”
3. The signal will be added to the waveform

## Slide 52: Wet Exercise 1
You will be required to:
  Implement modules using a given logic gate library
  Simulate them
The workshops cover all the syntax needed to solve the wet exercises

## Slide 53: Workshop #2 Cheat Sheet
Integer literals:
  <width'><signed><radix> value
Bitwise operators:
  &, |, ~, ^, ~^
Shift: <<, >>
Concurrent assignments:
logic signal1, signal2, signal3;
assign signal3 = signal1 | signal2;

## Slide 54: Workshop #2 Cheat Sheet
Initial:
always_comb:
initial begin
<statement1>;
# time_to_wait
<statement2>;
# time_to_wait
...
end
always_comb begin
<statement1>;
<statement2>;
...
end

## Slide 55: Workshop #2 Cheat Sheet
Parameter:
Local parameter:
parameter param1 = 1;
localparam param1 = 1;

## Slide 56: Full Adder Implementation using Two Half Adders

## Slide 57: Questions?