## Slide 1: SystemVerilog HDL Workshop #3
044252 - Digital Systems and Computer Structure

## Slide 2: Topics Covered Last Time
Hardware Description Languages
SystemVerilog Building Blocks:
  Values / Number representation
  Bitwise operators
  Module implementation
    Module instantiation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Test benches and simulation

## Slide 3: Topics Covered Last Time
Hardware Description Languages
SystemVerilog Building Blocks:
  Values / Number representation
  Bitwise operators
  Module implementation
    Module instantiation
    Concurrent assignments
    Procedural blocks
  Parameters
Parallelism in HDL
Test benches and simulation

## Slide 4: Module Instantiation - Recap
2-bit wide mux from two 1-bit muxes
  module mux2to1_2 (
  output logic [1:0] O,
  input logic [1:0] A,
  input logic [1:0] B,
  input logic sel
  );
  mux2to1 mux0 (.out(O[0]), .sel(sel), .A(A[0]), .B(B[0]));
  mux2to1 mux1 (.out(O[1]), .sel(sel), .A(A[1]), .B(B[1]));
  endmodule
B[1:0]
sel
O[1:0]
A[1:0]
A]0[
B]0[
A]1[
B]1[

## Slide 5: Concurrent Assignments - Recap
Connect a wire to a combinational logic or another wire
When the right-hand-side of an assignment changes, it immediately flows through to the left-hand-side wire
Syntax:
logic signal;
assign signal = 1'b0;
logic signal1;
logic signal2;
assign signal2 = signal1;

## Slide 6: Procedural Blocks - Recap
Sequential: all statements inside the block are executed sequentially
  One line after the other
Two procedural constructs:
initial begin
<statement1>;
# time_to_wait
<statement2>;
# time_to_wait
...
end
always_comb begin
<statement1>;
<statement2>;
...
end
initial:
always_comb:

## Slide 7: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 8: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 9: Relational Operators
All of these return a 1-bit logical value (true/false or ‘x’)
Meaning | Operator
Less than | <
Less than or equal to | <=
Greater than | >
Greater than or equal to | >=
Equal to | ==
Not equal to | !=

## Slide 10: Logical Operators
Used for conditions
Operands evaluated to 1-bit value: 0 (false), 1 (true) or x
Result is 1-bit value: 0 (false), 1 (true) or x
Meaning | Operator
Logical AND | &&
Logical OR | ¦¦
Logical NOT | !

## Slide 11: Logical Operators
logic A, B, C;
assign A = 1'b1;
assign B = 1'b0;
assign C = 1'bx;
Examples:
false | true && false  | A && B 
true | true ¦¦ true  | A ¦¦ !B 
x | x ¦¦ false  | C ¦¦ B 
false | x && false  | C && B 

## Slide 12: SystemVerilog Operator Precedence

## Slide 13: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 14: Conditional Statements: The if Statement
Used in procedural blocks
Syntax:
if (condition1) begin
<statement1>;
end
else if (condition2) begin
<statement2>;
end
else begin
<statement3>;
<statement4>;
end

## Slide 15: Reminder: Mux Implementation
module mux (
output logic out,
output logic outn,
input logic [1:0] in,
input logic sel
);
logic out1, out2, selb;
and a1 (out1, in[0], sel);
not i1 (selb, sel);
and a2 (out2, in[1] , selb);
always_comb begin
out = out1 | out2;
end
assign outn = ~out;
endmodule
in
2
In[0]
In[1]
outn

## Slide 16: The if Statement - Example
Mux Module:
A
B
Q
sel
module mux (
input logic A,
input logic B,
input logic sel,
output logic Q
;(
always_comb begin
if (sel == 1'b0) begin
Q = A;
end
else begin
Q = B;
end
end
endmodule
0
1
Notes: בדומה לסדנה הקודמת יצרנו כאן מוקס, רק שהפעם הקוד הרבה יותר קצר, ברור והמיפוי בקצה הוא אותו המיפוי

## Slide 17: Conditional Statements: The case Statement
Used in procedural blocks
Syntax:
case (<signal/expression>)
<value1>: begin
<statement1>;
end
  <value2>: begin
  <statement2>;
  <statement3>;
  end
default: begin
<statement4>;
end
endcase

## Slide 18: The case Statement - Example
module case_example (
input logic A,
input logic B,
input logic [1:0] w,
output logic Y
;(
always_comb begin
case (w)
2'b00: Y = A & B;
2'b01: Y = A | B;
2'b10: Y = A ^ B;
default: Y = ~B;
endcase
end
endmodule
A
B
Y
w
00
2
01
10
11

## Slide 19: Conditional Statements: casex, casez
Variants of case Statements:
  casex and casez
casez – ? and z are considered as don’t cares [0,1,z]
casex – ?, x and z are considered as don’t cares [0,1,x,z]
Example:
casez(w)
2'b1?: A = B + C;
2'b01: A = B ^ C;
default: A = B – C;
endcase
When using casez or casex we will use ? As don’t cares of 0/1
Notes: למה חשוב ערך דיפולטי?

## Slide 20: A Not-To-Do Example
module bad_mux (
input logic A,
input logic B,
input logic sel,
output logic Q
;(
always_comb begin
if (sel == 1'b1) begin
Q = A;
end
end
endmodule
A
Q
sel
G
I
O
Latch
Notes: מאחר ולא כיסינו את כלל האפשרויות יווצר לנו לאצ' אשר ישמור את הערך הקודם של קיו מאחר והערך של קיו לא משתנה ולא מוזן מהכניסות.
צריך לשמור את הערך הקודם ולכן יווצר רכיב זכרון

## Slide 21: Complete Assignments
always_comb should NOT be used for memory elements!
  If a signal is not assigned in a certain flow, a memory element is implicitly created to preserve the previous value
  Usually, this is a bug!
When using always_comb, always use complete assignments, i.e., assign values to all signals in all logic flows!

## Slide 22: Complete Assignments: Guidelines
“if” statements
  Use “else”
“case” statements
  Use “default”
General solution
  Use default assignments
always_comb begin
Q = 1'b0;
if (sel == 1'b1) begin
Q = A;
end
end
‘0’
A
sel
0
1
Q
Otherwise there might be uncovered options which lead to a bug.
Notes: באג במג'יק של הוק ריבר

## Slide 23: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 24: Flip Flop: Reminder
Notes: סט – להכיל ערך של 1 בפליפלופ בתחילת עולם
כליר – להתחיל ערך של 0

## Slide 25: The always_ff Statement
always_comb: implements an asynchronous/ combinatorical block
always_ff: implements a synchronous block
clk

## Slide 26: The always_ff Statement (without Reset)
Syntax:
always_ff @(posedge clk) begin
<sync statement1>;
<sync statement2>;
end
Sensitivity List
Sync Statements (on clock rise)
Notes: רשימת רגישויות – מתי להריץ את אבן היסוד

## Slide 27: always_ff Example: Implementing a Flip-Flop
logic a, in;
always_ff @(posedge clk) begin
a <= in;
end
clk
in
a
‘1’
‘0’
‘0’

## Slide 28: The always_ff Statement with Reset
Syntax:
always_ff @(posedge clk) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
With Synchronous Reset:
Initialization Statements (on reset)
Sensitivity List (no reset!)
Sync Statements (on clock rise)
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
With Asynchronous Reset:
Initialization Statements (on reset)
Sensitivity List
Sync Statements (on clock rise)
Notes: ריסט אסינכרוני – תגובה מיידית
הפסקה

## Slide 29: always_ff Example: Implementing a Flip-Flop with Reset
logic a, in;
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
a <= 1'b0;
end
else begin
a <= in;
end
end
rst
clk
in
a
‘1’
‘0’

## Slide 30: Assignment in an always_ff Block
In always_comb, we use a blocking assignment (= operator):
In always_ff, we use a non-blocking assignment (<= operator):
logic a, in;
always_comb begin
a = in;
end
logic a, in;
always_ff @(posedge clk) begin
a <= in;
end

## Slide 31: Procedural Assignments
Occur within procedural blocks such as always_comb, always_ff and initial
Triggered when the flow of execution reaches them
Blocking/Non-blocking
  Blocking assignment statement (= operator) acts much like in traditional programming languages. The whole statement is done before control passes on to the next statement
  Non-blocking assignment statement (<= operator) evaluates all the right-hand sides for the current time unit and assigns the left-hand sides at the end of the procedural block
Notes: מתי נבחר בלוקינג אל מול נון בלוקינג
כשנרצה השמה מיידית – בלוקינג
כשנרצה השמה בסיום המערכת – נון בלוקינג

## Slide 32: Example – Non blocking
module shifter(
input logic in,
input logic clk
;(
logic A, B, C;
always_ff @(posedge clk) begin
A <= in;
B <= A;
C <= B;
end
endmodule
A
clk
in
B
C
Notes: טבלת אמת
In = 0, A =1, B = 1, C = 1

## Slide 33: Example – Blocking
module bad_shifter(
input logic in,
input logic clk
;(
logic A, B, C;
always_ff @(posedge clk) begin
A = in;
B = A;
C = B;
end
endmodule
B
C
A
clk
in

## Slide 34: Assignment Summary
Synchronous logic: Use non-blocking statements with always_ff blocks sensitive only to rising clock edge to mimic parallel synchronous logic.
Combinational logic: Use blocking statements inside always_comb blocks with to mimic logic flow of combinational logic.

## Slide 35: Assignment: A Question From an Exam (Winter '18-'19)
Notes: מה זה 0x?
תשובה ה

## Slide 36: Example: Synchronous and Asynchronous Logic
A
clk
B
or_out
and_out
Synchronous Logic
Asynchronous/Combinatorical Logic
rst
A
A
B

## Slide 37: Example: Sync. and Async. Logic
module my_module (
input logic clk,
input logic rst,
output logic A,
output logic B
;(
  logic and_out, or_out;
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= or_out;
  B <= and_out;
  end
  end
  always_comb begin
  and_out = A & B;
  or_out = A | B;
  end
endmodule
Asynchronous/Combinatorical Logic
Synchronous Logic
Notes: מה ניתן לשנות בקוד כדי להשתמש רק בבלוק סינכרוני

## Slide 38: Example: Sync. and Async. Logic: Another Implementation
module my_module (
input logic clk,
input logic rst,
output logic A,
output logic B
;(
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= A | B;
  B <= A & B;
  end
  end
endmodule
Asynchronous &
Synchronous Logic

## Slide 39: Example: Sync. and Async. Logic: Synthesis error
module my_module (
input logic clk,
input logic rst,
input logic C,
output logic A,
output logic B
;(
logic d;
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= A | d;
  B <= A & B;
  end
  if (C == 1) begin
  d <= 1'b1;
  end
  end
endmodule
Notes: מה הבעיות שיווצרו בקטע הקוד הנל?
אנחנו עלולים להשתמש בd לפני שהוא אותחל אין else statement לd מה שיגרום לכך שישנם מסלולים אשר d אינו מאותחל בהם ואין לו ערך דיפולטי במצב של reset.
הסיתנזה עלולה לחשוב שd משמר את הערך שלו מה שיגרום ליצירת ff נוספים ופגיעה בביצועים בגלל דיליי

## Slide 40: Example: Sync. and Async. Logic: Synthesis error
There are 3 types of synthesis issues that may arise in this design:
“Variable d used before assigned” :
  This occurs because d is used in A <= A | d; before being guaranteed an initial value when C == 0.
“Variable d is not fully assigned in all paths”.
  The assignment to d only happens conditionally (if(c)) with no else clause or reset.
“Synthesis assumes d retains its value”
  When d is not updated in a cycle, tools assume it holds its previous value via a flip-flop.
  While technically legal, this can result in:
    Unintended stateful behavior.
    Incorrect logic if the user expected a purely combinational update.
    Performance delay.

## Slide 41: Agenda
More operators
Conditional statements
Synchronous logic and assignments
Test benches for synchronous logic

## Slide 42: Test Bench: Generating a Clock Signal
initial begin
Clock = 1'b0;
end
...
always begin
#10 Clock = ~Clock;
end
Clock
always statement: runs in an endless loop
Notes: מה זמן המחזור של השעון במקרה הזה?

## Slide 43: Test Bench: The Repeat Loop
  Used in an initial block to repeat statements.
  Syntax:
  Example: Waiting for 4 clock cycles
initial begin
repeat(4) begin
@(posedge clk);
end
end
repeat(num_of_times) begin
<statement1>;
<statement2>;
end

## Slide 44: Example: Sync. and Async. Logic: Another Implementation
module my_module (
input logic clk,
input logic rst,
output logic A,
output logic B
;(
  always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  A <= 1'b0;
  B <= 1'b1;
  end
  else begin
  A <= A | B;
  B <= A & B;
  end
  end
endmodule
Asynchronous &
Synchronous Logic

## Slide 45: Test Bench: Full Example
module my_module_tb;
logic clk, rst;
logic A, B;
my_module inst(.clk(clk), .rst(rst), .A(A), .B(B));
always begin
#10 clk = ~clk;
end
initial begin
clk = 1'b0;
rst = 1'b1;
@(posedge clk);
7#
rst = 1'b0;
repeat(2) begin
@(posedge clk);
end
end
endmodule

## Slide 46: Test Bench: Full Example
Notes: הבהרה מאוד מאוד מאוד חשובה על סנכרון בין סיגנלים לשעון! לדוגמה, לא יקרה מצב בו סיגנל ריסט עולה בירידת שעון

## Slide 47: Another Example: Simple Counter
current_counter
clk
next_counter
+1

## Slide 48: Another Example: Simple Counter
logic [3:0] current_counter;
always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  current_counter <= 4'b0;
  end
  else begin
  current_counter <= next_counter;
  end
end
always_comb begin
next_counter = current_counter + 1;
end
current_counter
clk
next_counter
+1
Notes: מה יקרה אחרי 16 מחזורי שעון לקאונטר? למה הוא יהיה שווה?

## Slide 49: Another Example: Simple Counter
logic [3:0] current_counter;
always_ff @(posedge clk, posedge rst) begin
  if (rst == 1'b1) begin
  current_counter <= 4'b0;
  end
  else begin
  current_counter <= current_counter + 1;
  end
end
current_counter
clk
+1

## Slide 50: A Question From an Exam (Spring '19)

## Slide 51
Notes: תשובה ג

## Slide 52: Questions?

## Slide 53: Workshop #3 Cheat Sheet
Logical operators: &&, ||, !
Relational operators: >, >=, <, <=, ==, !=
if statement:
if (condition1) begin
<statement1>;
end
else if (condition2) begin
<statement2>;
end
else begin
<statement3>;
<statement4>;
end

## Slide 54: Workshop #3 Cheat Sheet
case statement:
casez: ? and z are considered as don’t cares [0,1,z]
casex: ?, z and x are considered as don’t cares [0,1,z,x]
case (<signal/expression>)
<value1>: begin
<statement1>;
end
  <value2>: begin
  <statement2>;
  <statement3>;
  end
default: begin
<statement4>;
end
endcase

## Slide 55: Workshop #3 Cheat Sheet
always_ff statement:
always_ff with reset:
Async. Reset: Sync. Reset:
always_ff @(posedge clk) begin
<sync statement1>;
<sync statement2>;
end
always_ff @(posedge clk) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
<reset statement1>;
end
else begin
<sync statement2>;
end
end

## Slide 56: Workshop #3 Cheat Sheet
Generating a clock signal:
repeat loop:
repeat(num_of_times) begin
<statement1>;
<statement2>;
end
initial begin
Clock = 0;
end
...
always begin
#10 Clock = ~Clock;
end