## Slide 1: SystemVerilog HDL Workshop #5
044252 - Digital Systems and Computer Structure

## Slide 2: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 3: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 4: Reminder – What is FSM?

## Slide 5: FSM – Writing Code
Declare states used for FSM
Write FSM using two procedural blocks:
  Synchronous – saves current state
  Asynchronous – sets next state and output signals (according to current state and optionally input signals)
Other helper procedural blocks can also be used

## Slide 6: FSM Template
module my_FSM_module (
input logic input1,
...
output logic outputN
;(
// Declaring the FSM states
typedef enum { idle_st, start_st } sm_type;
// Declaring signals for the next & current state
sm_type current_state;
sm_type next_state;
// ...
endmodule

## Slide 7: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 8: FSM – Async Logic
always_comb begin
next_state = current_state;
output1 = 1'b0;
...
outputN = 1'b0;
case (current_state)
idle_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
start_st: begin
next_state = ...;
output1 = ...;
...
outputN = ...;
end
...
endcase
end
Default Assignments

## Slide 9: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 10: Control and Datapath Separation
Signals are classified into two categories:
  Data
    Usually buses (wide vectors)
    Common units: FAs, mux, ALU, …
  Control
    Usually single bits
    Common units: FSM
Data Processor
Controller
Data In
Data Out
Control
Status
External Status
External Control
Notes: בלוקים בסיסטם ורילוג מתחלקים בעיקר לשני סוגים
בקונטרולר תהיה מכונת מצב שתספק סגנלי קונטרול
ביחידה האריטמתית תספק את הסטטוס לקונטרולר

## Slide 11: Agenda
FSM – reminder
Control and datapath
UART – reminder
Summarizing example

## Slide 12: תקשורת על חוט יחיד
חוט טלפון, רשת מקומית, ...
במקום חוטי REQ, ACK:
  נשתמש בשעון איטי הרבה יותר מהשעונים הפועלים בשני הקצוות
  נסנכרן אותם מידי פעם:
גם זו קרויה "תקשורת אסינכרונית" אבל בעצם היא קצת סינכרונית
פרוטוקול תקשורת UART: Universal (Synchronous) Asynchronous Receiver/Transmitter
נהוג ביציאת COM של ה-PC
אפשרות אחרת (נהוגה ברשת מקומית מהירה): נקודד את השעון יחד עם הנתונים, למשל “Manchester Code”
Notes: מתחיל מ1, בתחילת שידור יורד ל0 לאורך טיביט קבוע בפרוטוקול
בדכ זמני מחזור יהיו קצרים מטי ביט, למה?
N=T/Tbit
כל סיגנל מידע ישלח טיביט זמן
סיגנל הסטופ ישלח בסוף

## Slide 13: UART – Transmitter FSM

## Slide 14: Agenda
FSM – reminder
UART – reminder
Summarizing example

## Slide 15: UART3 Protocol
In this workshop, we will plan a UART transmitter with a few minor changes:
  3-bit word instead of an 8-bit word
  Sends a parity bit
stop | stop | stop | parity | parity | parity | bit3 | bit3 | bit3 | bit2 | bit2 | bit2 | bit1 | bit1 | bit1 | start | start | start
baud time
Tx transmitter
Notes: מה הטיביט כאן לפי הדוגמה הזו ?
נשלח גם ביט פריטי – זוגיות – ויידוא תקינות
לשרטט את המודול – כניסות – סטארט, קלוק, אאוט, מידע וריסט
מכונת מצבים, יחידת מונה (מה היא עושה?), יחידה אריטמתית
כמה סוגי מידע יש לנו?
למה נבצע את המימוש בשני מוקסים שונים?

## Slide 16: Summarizing Example: UART3
Notes: כמה מחזורי שעון יקח לי לחשב את ביט הזוגיות?
למה נרצה פריטי קליר?
למה נרצה פריטי אנייבל? מאחר ואנחנו שולחים את סיגנלי המידע מספר פעמים

## Slide 17: Top Level and Signal Declarations
module UART3 (
input logic clk,
input logic rst,
input logic [2:0] A,
input logic start,
output logic out
;(
parameter N = 3;
logic counter_done;
logic counter_clear;
logic [1:0] A_sel;
logic [1:0] out_sel;
logic parity_clr;
logic parity_enable;
UART3_fsm fsm_u(
.clk(clk),
.rst(rst),
.start(start),
.counter_done(counter_done),
.counter_clear(counter_clear),
.A_sel(A_sel),
.out_sel(out_sel),
.parity_clr(parity_clr),
.parity_enable(parity_enable)
;(
UART3_counter #(
.N(N)
) cnt_u (
.clk(clk),
.rst(rst),
.counter_clear(counter_clear),
.counter_done(counter_done)
;(
UART3_arith arith_u(
.clk(clk),
.rst(rst),
.A(A),
.A_sel(A_sel),
.out_sel(out_sel),
.parity_clr(parity_clr),
.parity_enable(parity_enable),
.out(out)
);
endmodule
Notes: הפסקה

## Slide 18: Simulations – Top Level
start
A[0]
A[1]
A[2]
parity
stop
Notes: מה מוכל בסיגנל איי? 110
מתחילים לשלוח מLSB

## Slide 19: Building the FSM
Build a Mealy FSM
Requirements:
  Receives several signals:
    clk
    rst (asynchronous)
    start
    counter_done
  Outputs:
    parity_clr
    parity_enable
    A_sel
    out_sel
    counter_clr

## Slide 20: UART3: FSM Design
start == 1 /
parity_clr=1
rst
Start bit
Idle
First bit
Second bit
Third bit
Parity
counter_done && start == 0
counter_done && start == 1 /
parity_clr=1
Start == 0
Stop bit
Defaults:
parity_clr = 0
A_sel = 0
out_sel = 2
counter_clr = 1
parity_enable = 0
!counter_done /
counter_clr=0
out_sel=1
counter_done /
out_sel=1
!counter_done /
counter_clr=0
out_sel=0
counter_done /
parity_enable=1
out_sel=0
!counter_done /
counter_clr=0
out_sel=0
A_sel=1
counter_done /
parity_enable=1
out_sel=0
A_sel=1
!counter_done /
counter_clr=0
out_sel=0
A_sel=2
counter_done /
parity_enable=1
out_sel=0
A_sel=2
!counter_done /
counter_clr=0
out_sel=3
counter_done /
out_sel=3
!counter_done /
counter_clr=0
Notes: איזה מכונה זו?

## Slide 21: FSM
module UART3_fsm ( input logic clk, input logic rst, input logic start, input logic counter_done, output logic counter_clear, output logic [1:0] A_sel, output logic [1:0] out_sel, output logic parity_clr, output logic parity_enable ); typedef enum { idle_st, start_bit_st, first_bit_st, second_bit_st, third_bit_st, parity_st, stop_bit_st } sm_type; sm_type current_state; sm_type next_state;

## Slide 22: FSM – Synchronous Logic
// FSM synchronous procedural block. always_ff @(posedge clk, posedge rst) begin if (rst == 1'b1) begin current_state <= idle_st; end else begin current_state <= next_state; end end

## Slide 23: FSM – Async Logic
always_comb begin next_state = current_state; parity_clr = 1'b0; A_sel = 2'd0; out_sel = 2'd2; counter_clear = 1'b1; parity_enable = 1'b0; case (current_state) idle_st: begin if (start == 1'b1) begin next_state = start_bit_st; parity_clr = 1'b1; end end start_bit_st: begin out_sel = 2'd1; if (counter_done) begin next_state = first_bit_st; end else begin counter_clear = 1'b0; end end
first_bit_st: begin out_sel = 2'd0; if (counter_done) begin next_state = second_bit_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end second_bit_st: begin out_sel = 2'd0; A_sel = 2'd1; if (counter_done) begin next_state = third_bit_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end

## Slide 24: FSM – Async Logic
third_bit_st: begin out_sel = 2'd0; A_sel = 2'd2; if (counter_done) begin next_state = parity_st; parity_enable = 1'b1; end else begin counter_clear = 1'b0; end end parity_st: begin out_sel = 2'd3; if (counter_done) begin next_state = stop_bit_st; end else begin counter_clear = 1'b0; end end
stop_bit_st: begin if (counter_done) begin if (start == 1'b0) begin next_state = idle_st; end else begin next_state = start_bit_st; parity_clr = 1'b1; end end else begin counter_clear = 1'b0; end end

## Slide 25: Simulations – FSM

## Slide 26: Arithmetic Unit
module UART3_arith (
input logic clk,
input logic rst,
input logic [2:0] A,
input logic [1:0] A_sel,
input logic [1:0] out_sel,
input logic parity_clr,
input logic parity_enable,
output logic out
);
logic parity;
logic A_out;
// A mux
always_comb begin
case (A_sel)
2'd0: A_out = A[0];
2'd1: A_out = A[1];
2'd2: A_out = A[2];
default: A_out = 1'b0;
endcase
end
// Out mux
always_comb begin
case (out_sel)
2'd0: out = A_out;
2'd1: out = 1'b0;
2'd2: out = 1'b1;
2'd3: out = parity;
default: out = 1'b0; // For simulation only
endcase
end
// Parity register
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
parity <= 1'b0;
end
else begin
if (parity_clr == 1'b1) begin
parity <= 1'b0;
end
else if (parity_enable == 1'b1)
begin
parity <= parity ^ A_out;
end
end
end
endmodule
Notes: איזה סוג ריסט הוא הפריטי קליר?

## Slide 27: Simulations – Parity

## Slide 28: Counter
module UART3_counter (
input logic clk,
input logic rst,
input logic counter_clear,
output logic counter_done
);
parameter N = 3;
logic [31:0] counter;
always_ff @(posedge clk, posedge rst) begin
if (rst == 1'b1) begin
counter <= 32'd0;
end
else begin
if (counter_clear == 1'b1) begin
counter <= 32'd0;
end
else if (counter < N - 1) begin
counter <= counter + 1;
end
end
end
always_comb begin
if (counter == N - 1) begin
counter_done = 1'b1;
end
else begin
counter_done = 1'b0;
end
end
endmodule

## Slide 29: Simulations – Counter

## Slide 30: Test Bench
module UART3_test; logic clk; logic rst; logic [2:0] A; logic start; logic out; UART3 #(.N(3)) uart ( .clk(clk), .rst(rst), .A(A), .start(start), .out(out) ;( initial begin clk = 1'b0; 5# rst = 1'b1; 10# rst = 1'b0; A = 3'b110; start = 1'b1; end always begin 5# clk = ~clk; end endmodule

## Slide 31: The Full Code
UART3_fsm fsm_u (…);
UART3_counter counter_u(…);
UART3_arith arith_u(…);
The full code is supplied with the workshop files
UART3.sv
UART3_fsm.sv
UART3_counter.sv
UART3_arith.sv
UART3_test.sv
UART3 uart3 (…);

## Slide 32: Debugging Tips Video
Hardware debugging is different than software debugging
  Waveform vs. tests / debug prints
The workshop code is supplied with a video which explains about debugging hardware
  Common mistakes
  How to track bugs using a waveform

## Slide 33: Exam Question
module mymodule (
input logic clk,
input logic rst,
output logic done
;(
parameter N = 3;
logic [31:0] w;
always_ff @(posedge clk, posedge rst)
begin
if (rst == 1'b1) begin
w <= 32'd0;
end
else begin
if (w < N - 1) begin
w <= w + 1;
end
else if (w == N - 1) begin
w <= 0;
end
end
end
always_comb begin
if (w == N - 1)
begin
done = 1'b1;
end
else begin
done = 1'b0;
end
end
endmodule

## Slide 34: Exam Question
module mymodule2 (
input logic clk,
input logic rst,
output logic out
;(
logic w1;
logic w2;
mymodule uut1 (clk, rst, w1);
mymodule #(.N(2)) uut2 (clk, rst, w2);
always_comb begin
if ((w1 == 1'b1) && (w2 == 1'b1)) begin
out = 1'b1;
end
else begin
out = 1'b0;
end
end
endmodule
After reset, how many clock cycles are between two rises of out signal?
Notes: באינסטנס הראשון כל כמה מחזורי שעון הוא יעלה – 3
באינסטנס השני כל כמה מחזורי שעון הוא יעלה – 2
לכן יעברו שישה מחזורי שעון בין שני עליות בסיגנל המוצא

## Slide 35: The Exam
One SV multiple-choice question (~5 points)
The material from the workshops and wet exercises is important. Implementation details from the wet exercises are not!
We are available for questions in the Moodle forum

## Slide 36: Questions?